## Slide 1: Single-crystal Bragg Peak Finding
Richard Waite
Oak Ridge Dev Meeting
Oct 23

## Slide 2: Why do it?
Finding peaks is the first step in any reduction
You need to find peaks to
Find a UB matrix to index peaks
  Lattice parameters (B matrix)
  Crystal orientation in lab frame (U Matrix)
Find satellite peaks to determine modulation vectors
Centering conditions
Calibrate the detector & sample positions

## Slide 3: Currently in mantid
Two approaches:
Detector-TOF space (FindSXPeaks)

## Slide 4: Currently in mantid
Two approaches:
Detector-TOF space
Q-space (FindPeaksMD)
Sort boxes by signal density above threshold
Add N peaks starting from densest boxes
Reject boxes too close to existing peaks

## Slide 5: Currently in mantid
Methods share common disadvantages
Not good for weak peaks
Arbitrary threshold (needs to be optimised for each sample)
Not looking at peaks wrt to local background
Method | Pros | Cons
FindSXPeaks | Fast | Find peaks in powder lines Spurious peaks due to noise Using stats on a single pixel (misses weak peaks) Requires data to be normalised by monitor Not suited for strongly varying background Arbitrary cutoff
FindPeaksMD | Good at finding strong peaks | Need to convert data to Q Not designed to find weak peaks Requires data to be normalised by monitor Not suited for strongly varying background

## Slide 6: A new approach needed
Requirements:
Find peaks in detector-TOF space
Takes into account local background (varies with scattering angle and wavelength)
Exclude powder lines  3D peak finding!
Not as sensitive to noise  group detector pixels
Use knowledge of peak shape and resolution
  TOF extent from back-to-back parameters
  Constrain peak size on detector
Prefer some statistical threshold rather than arbitrary cut-off

## Slide 7: A new algorithm FindSXPeaksConvolve
Inspired by traditional blob detection methods (Laplacian convolution, difference of Gaussians etc.) and 2D image plate integration methods in x-ray diffraction.
Convolves data (XY-TOF) in each RectangularDetector with 3D shoebox integration kernel (with background shell)
  TOF extent from NFWHM of BackToBackExponential at center of detector and spectrum
  XY hard-coded for now (could use different one per bank)
Finds contiguous bins with I/sigma > threshold
Reject peaks number of bins below fractional size (1/8) of kernel
Assigns peaks to highest counts in shoebox placed at largest I/sigma bin in each region

## Slide 8: Comparison
FindSXPeaks
FindSXPeaksConvolve

## Slide 9: Performance of integration
Good agreement of intensity
Slightly underestimate I/sigma (especially weak peaks I/sigma < 10)
  Possibly due to non-optimised shoebox size.

## Slide 10: Next steps
Dynamic shoebox integration on predicted peak positions
  Adjust peak size to maximise I/sigma?
How to resolve partially overlapping peaks?
Speed it up (currently in python…)

## Slide 11: Thank you!

## Slide 12: Finding good back-to-back parameters